## Slide 1: Mastor_detecter*
How does it work?
*in serious need of a better name

## Slide 2: Table of contents
Data processing
  Decimation
  Whitening
  Combination
Detector
  Obtaining putative detections
    Raven Band Limited Energy Detectors (BLED)
    Algorithm
  Validation
    Compare to ground truth to assess accuracy of Raven detectors and algorithm
    Training data
Model
  Feature extraction
  Cross-validation
Outputs
  Metrics
  Data
  Assumptions

## Slide 3
Data for analysis
Data processing
Run Raven detector and algorithm
GT data
Compare detector w GT
Training data
* Training data is composed of boxes labeled with positive (1) and negative (0) detections. It also contains measurements of sound and image data from the clip (features). These data are used by the model for binary classification, which functions as a flexible filter for consistent interference to the dataset.
Training data
Create random forest models
Randomly sample 75% of data to build model.
Undersample 0s to same size as 1s to fix class imbalance
Randomly sample 25% of data to test performance of generated model
CV x60
Apply models to dataset
Threshold and manually review for TPs
Threshold and compare detector w GT
OR
Dataset of analyst validated TPs
Estimated total counts based on accuracy (TPR)
Detector performance metrics (TPR, FPR), accuracy for each mooring
1.
2.
Accuracy metrics derived from GT’d data only applicable on a training set that is a representative sample of the whole data population. Or has a consistent differential
If performance is satisfactory
If data has GT
If unsatisfactory
If unsatisfactory
Add more data to training set
*
Feature extraction
Add more informative features
Change Raven detector or algorithm
Change whitening parameters
Detector performance metrics (TPR, FPR), accuracy for each mooring
If unsatisfactory
If performance is satisfactory
Step 2.
Training data
Unseen data
If performance is satisfactory
If data is unseen
Step 2.

## Slide 4: Data processing: Decimation
The first transformation performed on data is decimation.
  Decimation is key for optimizing run time of script and minimizing disk space required.
Data is decimated according to user preference
  Our included data comes from AURALS (16384Hz sample rate)
  Decimation factor can be set by user depending on signal of interest and instrument specification. We chose a decimation factor of 16 to obtain a signal of 1024Hz sample rate.
  Decimation is performed iteratively based on the prime factors of your decimation factor. A decimation factor of 16 will be decimated x2, 4 times.
    Make sure you choose a divisor that will result in an integer sample rate. Divisors with more prime factors with decimate more quickly.
  Decimated data will be written to your drive as a subfolder of your provided data.

## Slide 5: Data processing: Whitening
Whitening is a transformation that can improve the performance of some detectors in noisy environments
There is no implementation of the Adaptive line enhancer (ALE) filter in R, so this step must be done manually in Raven 1.5
  The script will map to the containing whitened data as long as naming conventions are followed.
Least mean squared and filter order parameter most effective to modify.
Because any performance gains seem incremental at best in the current version of the detector, as well as the inconvenience of having to implement it manually, whitening is currently not a recommended data transformation.

## Slide 6: Data processing: Combination
In order to reduce the overhead of accessing Raven Pro 1.5 through API, sound files are combined to bundle up the call to the Raven band limited energy detectors (BLEDs).
Combination happens automatically, but takes up some extra disk space
Large files may be broken up into chunks according to user specification.
These combined sound files are also useful for ease of access when loading up data for manual review of data.

## Slide 7: Detector: Raven BLEDs
Found that more narrowband BLED resulted in higher chance for detection of SOI, and can be used as a pitch tracker to provide an initial filter for detections
Each species has a suite of Raven BLEDs that each correspond to a portion of the desired frequency range. These are created by the user in Raven, but called through the script.